Document and Content Analysis
Character Recognition
Thomas Breuel

---
OCR steps
- cut apart pages into text lines and images
- cut apart each text line into characters
- recognize each character
- re-assemble the page text

---
page → text lines
(Talked about this last time.)

---
original page
book/0005.png

---
text lines
0005/0001.png
0005/0002.png
0005/0003.png
0005/0004.png
0005/0005.png
0005/0006.png ...

---
text line → characters
How do you cut apart a line of text into characters?

---
segmentation by projection

---
segmentation by projection
compute segmentation
components
label connected
components
“and” with original
binary image

---
segmentation by projection

---
segmentation by projection
- input
  - binary text line image
- algorithm
  - project along the vertical axis
  - find low/zero regions in projection profile
  - generate an image where those “bands” are set to 0, all other values are 1
  - label connected components
  - intersect the connected components with the original binary image
- output
  - color-coded segmentation image

---
recognition by template matching

---
recognition by template matching
Handel, 1933

---
recognition by template matching
- idea
  - put different templates on top of each character
  - see which template matches best
  - return the identity associated with the template

---
correlation
(Simple) correlation is like convolution, except that the offset is added,
rather than subtracted.
(Normalized or statistical cross-correlation is something different.)

---
template matching

---
detection threshold

---
template matching
- above example
  - pick a template and slide it across entire image
  - inefficient: many places matched that needn't be
- real-world recognition
  - partition the image into character subimages
  - take each character
  - slide the template around each character a little bit
  - compute the maximum correlation as quality-of-match
  - return the best matching template

---
template matching
template_e
template_a
template_c

---
recognition by template matching

---
template matching

---
text line recognition
- text line segmentation
  - compute vertical projection profile
  - threshold
  - segment into characters
- recognition
  - extract each character
  - match against a list of templates
  - return the character code of the best-matching template

---
Are we done?

---
problems
- segmentation by projection
  - italics, ligatures, kerning
  - touching / broken characters
- recognition by template matching
  - slow
  - bad recognition accuracy
    - size, shape variation, noise, italics
    - new fonts etc.
    - thresholds?

---
better segmentation

---
typographic phenomena
To
aﬃne
kerning
touching characters &
ligatures
light
italics

---
image degradation

---
“simple approach”
- assume that segmentation mostly works
- try to recognize things
- check the resulting words against dictionary
- if it doesn't fit...
  - backtrack...
  - try to identify characters that can be split/merged...
  - try to recognize again
- properties
  - fast, intuitive... but requires a lot of tuning
  - doesn't generalize well to severely degraded

---
better text line segmentation
- better cutting algorithm
  - allow curved cuts
  - dynamic programming algorithm finds optimal paths
- two step
  - first, cut characters apart
  - second, group character parts together

---
oversegmentation

---
cuts by dynamic programming
- step = 1
- diagonal = +0.5
- black = +2
2.5
2
2.5
2
2.5
1
1
1
1
1
1
1
1
1
1
1

---
cuts by dynamic programming
- step = 1
- diagonal = +0.5
- black = +2
14.5
15
15.5
14
14.5
11.5
12
12.5
13
13.5
10.5
11
11.5
12
12.5
9.5
10
10.5
8
8.5
9
7
7
7.5
8
6
6
6.5
5
5
5
7.5
4
4
4
4
6.5
6
6
6
3
3
3
3
5
5
5
5
5
2
2
2
2.5
2
2
2
2
4
4
4
2
1
1
1
1
1
1
1
1
1
1
1

---
cuts by dynamic programming

---
cuts by dynamic programming
- input
  - image of a text line
- algorithm
  - compute center line of text line
  - propagate costs inward
  - trace paths outward from center line
    - this guarantees a path at every point
  - plot costs vs x-position
  - pick those cut paths that have a local min.
- output
  - collections of cut-paths through the image

---
cuts vs characters
darn

---
segmentation graph
- consider each cut a node in a graph
- for every pair of cuts no more than n apart
  - consider the edge between the two nodes...
  - associate it with the image delimited by the cuts

---
segmentation graph

---
segmentation graph
- nodes
  - cuts
- edges
  - images delimited by cuts
- small encoding of possible segmentations
  - exponential # segmentations possible
- path through the graph
  - a particular interpretation of the input

---
after classification
*
r
*
*
*
a
n
d
*

---
after classification
clarri, clarn, darri, darn, clam, dam
r
r
i
l
c
a
n
d
m

---
segmentation graph interpretation
- classifications aren't perfect
- each classification has a “cost”
- what's the best interpretation of the graph?

---
after classification
clarri, clarn, darri, darn, clam, dam
r
r
0.7
i
l
c
0.8
2.3
0.3
1.1
a
n
d
0.5
0.2
m
0.3
1.4
min cost = 0.3 + 0.5 + 0.3 + 0.2 = 1.3

---
questions
- how should we compute the “costs”?
- should we add them?
- can we compare different paths?
- what about paths with different lenghts?
- what about non-characters?
- what about dictionaries?
- relationship to HMMs?

---
better classification

---
classifiers
0.3
9.5
-7.1
255.3
244
-1
-1
0
1
17.4
class 17

---
nearest neighbor classifier
def classifier(x):
    best_c = -1
    best_d = infinity
    for v,c in training_examples:
        d = dissimilarity(v,x)
        if d<best_d:
        best_d = d
        best_c = c
    return best_c

---
classifiers
- a classifier assigns classes to input patterns
- classifiers classify based on training data
- new patterns are often not identical to known ones, merely similar
- classifiers need to generalize to such novel patterns
- input patterns are typically real vectors of fixed dimension

---
what makes classification hard?
- variations in position, size, orientation
- noise and image degradation
- large number of fonts
- context-dependence of interpretation

---
a
example: size / orientation
a
a
a
a

---
o
example: context
lower case “o”
capital “O”
mathematical circle symbol
digit “0”

---
To
example: context
lower case “o”
capital “O”
mathematical circle symbol
digit “0”

---
example: font variability
- similar to humans
- very different as bit patterns

---
dealing with variability & context
- noise removal & preprocessing
- text line modeling
- size normalization
- slant normalization
- context-dependent classifiers

---
text line modeling
- char 1: ascender
- char 2: no ascender/descender

---
size normalization
- classifier takes fixed dimensional input
- characters come in all sizes
- absolute size/position is meaningless
- relative size/position is important
- how do we reconcile this?

---
approach 1: scanning
- locate the baseline and x-height
- rescale the line s.t. the x-height is 10 pixels
- make the window 30x30
- place baseline at y=10, x-height at y=20
  - (why not simply make the whole line 30 pixels high?)
- center on characters and mask neighbors

---
approach 2: extract, encode, resize
+ y-pos/x-height + height/x-height
- extract each character
- rescale to fit into 30x30 bounding box
- encode y-position relative to baseline
- encode height
- units: x-height

---
normalization by moments
- fit into target image of size w x h
- compute the centroid of the character
  - put the centroid at the center of the image
- compute the trace of the covariance matrix
  - rescale to given value
- compute the slant of the character
  - apply a skew transformation to achieve zero slant

---
normalization by bounding box
- fit into target image of size w x h
- two possibilities
  - rescale anisotropically so that the character fills the target
  - rescale by the minimum horizontal / vertical scale
- more possibilities
  - switch between anisotropic and isotropic
  - don't scale up, only scale down

---
image scaling
- image scaling by subsampling
  - doesn't work well by itself
  - think about thin lines
- image scaling by antialiasing + subsampling
  - the correct thing to do
  - works significantly better

---
labeling tools

---
summary

---
text line recognition
- simple approach
  - projection-based segmentation into characters
  - template matching for character recognition
  - dictionary + backtracking
- better approach
  - dynamic programming segmentation
  - segmentation graph
  - best path search
  - shape normalization prior to classification